## Slide 1
AVR ASSEMBLY LAB
Simple student guide
for SimulIDE
ATmega328P / AVRA-compatible assembly
7 experiments from GPIO to ADC, PWM and interrupts
Student edition
Follow the 7 experiments in order. Modify hardware, run and observe.
01
SIMULIDE + AVR ASSEMBLY

## Slide 2
AVR ASSEMBLY LAB / SIMULIDE
How to use this guide
Each experiment ends with an observable change in a register, pin or component
WHAT YOU WILL PRACTISE
Build and run AVRA-compatible .asm programs in SimulIDE
Trace an instruction through a register, an I/O pin and a component
Progress from GPIO output to timer PWM, ADC and interrupts
Leave with a reusable circuit and a working integrated project
Working rule
Change one line at a time. Predict the result, then run it.
USE THIS CYCLE FOR EVERY EXPERIMENT
01
Read
objective and circuit
02
Type
assembly code
03
Run
in SimulIDE
04
Observe
LED, register or scope
05
Record
one changed value
ATmega328P / AVRA-compatible assembly
02

## Slide 3
AVR ASSEMBLY LAB / SIMULIDE
Hardware changes by experiment
Build the basic circuit first. For each step, add or move only the part shown here
Experiment | Hardware modification | What you should see
1 | Add LED and 330 Ω resistor: PB0 → resistor → LED → GND | PB0 turns the LED on and off
2 | No change. Keep the PB0 LED circuit. | The same LED blinks
3 | Add push button: PD2 → button → GND | Button controls the PB0 LED
4 | Add LEDs and resistors at PB1, PB2 and PB3. Keep PB0. | One lit LED moves across PB0 to PB3
5 | Move or add PWM LED at PD6 / OC0A. Attach scope to PD6. | Brightness and waveform change
6 | Add potentiometer. Ends: +5 V and GND. Wiper: PC0 / ADC0. Keep PD6 LED. | Pot position changes brightness
7 | Keep potentiometer and PD6 LED. Add button: PD2 / INT0 → GND. | Button toggles the ADC-to-PWM system
Keep one common ground. Reuse the existing circuit unless this table tells you to add or move a part.
Hardware changes for the seven experiments
03

## Slide 4
AVR ASSEMBLY LAB / SIMULIDE
Before the lab
Use the provided tools and keep each experiment in its own project folder
WHAT YOU NEED
Lab PC
course workspace
SimulIDE
circuit + debugger
AVRA
.asm to .hex
ATmega328P
same device each time
YOUR PROJECT FOLDER
project/
exp01_led.asm
exp01_led.hex
avr_lab.sim1
# assemble your source
avra exp01_led.asm
# load the .hex in SimulIDE
YOUR LAB LOOP
Write
assembly source
Assemble
AVRA creates .hex
Load
firmware in SimulIDE
Observe
circuit, registers, scope
Change
one line or one value
Keep one copy of your working .asm and .hex files before starting the next experiment.
Student setup / source → .hex → SimulIDE circuit
04

## Slide 5
AVR ASSEMBLY LAB / SIMULIDE
Reusable SimulIDE circuit
Keep the MCU and instruments in place. Add capability by changing code and connecting only the needed component
ATmega328P
one MCU for every experiment
single-step / breakpoints / registers
Push button
PD2 / INT0
Potentiometer
PC0 / ADC0
Status LED
PB0
Running LEDs
PB0–PB3
PWM LED + scope
PD6 / OC0A
Common ground and supply stay consistent across all experiments.
Use the same circuit across the experiments
GPIO output → input → pattern → PWM → ADC → interrupt
Pin map used by the seven experiments
05

## Slide 6
AVR ASSEMBLY LAB / SIMULIDE
The assembly-to-hardware mental model
Make every register write visible before introducing the next peripheral
DDRx
Direction register
1 means output
0 means input
PORTx
Output value when driving
Pull-up enable when reading
PINx
Read the physical pin
Use for button state
Peripheral regs
Timer, ADC and interrupt
configuration
Instruction
SBI / CBI / OUT
Register
DDRB / PORTB
Pin
PB0 goes HIGH
Component
LED changes
Single-step example: LDI R16, 0x01 then OUT PORTB, R16 then watch PB0.
Core register model before timers and ADC
06

## Slide 7
EXPERIMENT 01 / AVR ASSEMBLY LAB
Experiment 1 / LED ON/OFF using GPIO
The first visible result: make one pin an output and drive it high
OBJECTIVE
Configure PB0 as an output
Set PORTB bit 0 high
Single-step and watch the LED turn on
CIRCUIT
PB0
330Ω
LED
GND
HARDWARE MODIFICATION
1. Place LED and 330 Ω resistor.
2. Connect PB0 → resistor → LED → GND.
EXPERIMENT 1 / GPIO OUTPUT
.include "m328pdef.inc"
.org 0x0000
rjmp RESET
RESET:
; Configure PB0 as output
sbi DDRB, PB0
; Make PB0 HIGH
sbi PORTB, PB0
LOOP:
rjmp LOOP
Student challenge: replace sbi PORTB, PB0 with cbi PORTB, PB0 and observe the result.
Experiment 1 / GPIO output
07

## Slide 8
EXPERIMENT 02 / AVR ASSEMBLY LAB
Experiment 2 / LED blinking using software delay
Introduce subroutines, counters and nested loops while keeping the same LED circuit
CONCEPT MAP
R18
outer count
R19
middle count
R20
inner count
DEC → BRNE
when the counter reaches 0, the next loop continues
HARDWARE MODIFICATION
Step: no hardware change. Keep the PB0 LED circuit.
Challenge: change ldi r18, 40 to ldi r18, 10.
EXPERIMENT 2 / SOFTWARE DELAY
.include "m328pdef.inc"
.org 0x0000
rjmp RESET
RESET:
sbi DDRB, PB0
MAIN:
sbi PORTB, PB0
rcall DELAY
cbi PORTB, PB0
rcall DELAY
rjmp MAIN
DELAY:
ldi r18, 40
D1:
ldi r19, 255
D2:
ldi r20, 255
D3:
dec r20
brne D3
dec r19
brne D2
dec r18
brne D1
ret
Experiment 2 / RCALL, RET, DEC and BRNE
08

## Slide 9
EXPERIMENT 03 / AVR ASSEMBLY LAB
Experiment 3 / Push button controls LED
Move from output to input with an internal pull-up and active-low logic
ACTIVE-LOW INPUT
Released
PD2 = HIGH
Pressed
PD2 = LOW
HARDWARE MODIFICATION
1. Keep the PB0 LED.
2. Add a push button:
PD2 → button → GND
3. The code enables the pull-up.
SBIC PIND, PD2
clear means pressed
set means released
Student challenge: reverse the logic so the LED turns off while the button is pressed.
EXPERIMENT 3 / INPUT + POLLING
.include "m328pdef.inc"
.org 0x0000
rjmp RESET
RESET:
sbi DDRB, PB0
cbi DDRD, PD2
sbi PORTD, PD2
MAIN:
; Skip next instruction if PD2 is LOW
sbic PIND, PD2
rjmp BUTTON_NOT_PRESSED
BUTTON_PRESSED:
sbi PORTB, PB0
rjmp MAIN
BUTTON_NOT_PRESSED:
cbi PORTB, PB0
rjmp MAIN
Experiment 3 / PINx, pull-up and SBIC
09

## Slide 10
EXPERIMENT 04 / AVR ASSEMBLY LAB
Experiment 4 / Running LED pattern
Use a register as a moving bit pattern and make the shift visible on four LEDs
DESIRED PATTERN
0
0
0
1
start
0
0
1
0
LSL
0
1
0
0
LSL
1
0
0
0
LSL
HARDWARE MODIFICATION
1. Keep the PB0 LED.
2. Add LED and 330 Ω resistor at PB1, PB2 and PB3. Connect each LED to GND.
Student challenge: add a reverse pattern using LSR, then alternate forward and reverse motion.
EXPERIMENT 4 / BIT PATTERN
.include "m328pdef.inc"
.org 0x0000
rjmp RESET
RESET:
ldi r16, 0x0F
out DDRB, r16
ldi r16, 0x01
MAIN:
out PORTB, r16
rcall DELAY
lsl r16
cpi r16, 0x10
brne MAIN
ldi r16, 0x01
rjmp MAIN
DELAY:
ldi r18, 30
D1:
ldi r19, 255
D2:
ldi r20, 255
D3:
dec r20
brne D3
dec r19
brne D2
dec r18
brne D1
ret
Experiment 4 / LSL, CPI, BRNE and subroutine reuse
10

## Slide 11
EXPERIMENT 05 / AVR ASSEMBLY LAB
Experiment 5 / PWM generation using Timer0
Let the timer generate the waveform while the CPU waits in a simple loop
HARDWARE PATH
Timer0
OCR0A
PD6 / OC0A
HARDWARE MODIFICATION
1. Move or add LED + 330 Ω: PD6 / OC0A → resistor → LED → GND.
2. Connect scope signal to PD6 and scope ground to GND.
OCR0A = 64 ≈25%
OCR0A = 128 ≈50%
OCR0A = 192 ≈75%
Student challenge: test 20, 64, 128, 200 and 255. Record brightness and waveform duty cycle.
EXPERIMENT 5 / TIMER0 PWM
.include "m328pdef.inc"
.org 0x0000
rjmp RESET
RESET:
; PD6 / OC0A output
sbi DDRD, PD6
; Fast PWM, non-inverting
ldi r16, (1<<COM0A1) | (1<<WGM01) | (1<<WGM00)
out TCCR0A, r16
; Clock / 64
ldi r16, (1<<CS01) | (1<<CS00)
out TCCR0B, r16
; Approximately 50% duty cycle
ldi r16, 128
out OCR0A, r16
MAIN:
rjmp MAIN
Experiment 5 / TCCR0A, TCCR0B and OCR0A
11

## Slide 12
AVR ASSEMBLY LAB / SIMULIDE
PWM and the oscilloscope
Use the waveform to connect a register value with a visible duty cycle and brightness change
TIMER COUNT
0
255
64
128
191
OCR0A chooses how long the output stays high during each timer cycle.
WAVEFORM EXAMPLES
25%
high
low
50%
high
low
75%
high
low
Before changing OCR0A, predict the oscilloscope trace. Then compare your prediction with the waveform.
Experiment 5 / waveform interpretation
12

## Slide 13
EXPERIMENT 06 / AVR ASSEMBLY LAB
Experiment 6 / ADC controls LED brightness
Map a potentiometer voltage to an 8-bit PWM value with a left-adjusted ADC result
SIGNAL PATH
Potentiometer
0–5 V
ADC0
10-bit result
ADCH
8-bit read
OCR0A
PWM duty
LED
brightness
WHY LEFT-ADJUST?
ADC output: 0 to 1023
PWM input: 0 to 255
10-bit
ADCH
8-bit
Left adjustment lets the program read ADCH directly and write it to OCR0A.
HARDWARE MODIFICATION
1. Pot end pins: +5 V and GND
2. Wiper: PC0 / ADC0. Keep PWM LED: PD6 / OC0A.
Experiment 6 / PC0 / ADC0 to PD6 / OC0A
13

## Slide 14
EXPERIMENT 06 / AVR ASSEMBLY LAB
Experiment 6 / ADC controls LED brightness
AVRA-compatible example: ADC0 conversion, wait for completion, then ADCH to OCR0A
EXPERIMENT 6 / COMPLETE ADC + PWM EXAMPLE
.include "m328pdef.inc"
.org 0x0000
rjmp RESET
RESET:
; PWM setup
sbi DDRD, PD6
ldi r16, (1<<COM0A1) | (1<<WGM01) | (1<<WGM00)
out TCCR0A, r16
ldi r16, (1<<CS01) | (1<<CS00)
out TCCR0B, r16
; ADC setup: AVcc, left adjusted, ADC0
ldi r16, (1<<REFS0) | (1<<ADLAR)
sts ADMUX, r16
ldi r16, (1<<ADEN) | (1<<ADPS2) | (1<<ADPS1) | (1<<ADPS0)
sts ADCSRA, r16
MAIN:
; Start ADC conversion
lds r16, ADCSRA
ori r16, (1<<ADSC)
sts ADCSRA, r16
WAIT_ADC:
lds r16, ADCSRA
; Wait while ADSC = 1
sbrc r16, ADSC
rjmp WAIT_ADC
; Read 8-bit ADC result
lds r17, ADCH
; ADC directly controls PWM
out OCR0A, r17
rjmp MAIN
CHECK YOUR UNDERSTANDING
ADMUX selects AVcc reference, left adjustment and ADC0
ADCSRA enables the ADC and sets the clock prescaler
ADSC starts a conversion
SBRC keeps waiting while ADSC is still set
ADCH becomes the new PWM duty value
If AVRA rejects a line-continuation expression, keep the bitwise expression on one line as shown here.
Experiment 6 / ADMUX, ADCSRA, ADCH and OCR0A
14

## Slide 15
EXPERIMENT 07 / AVR ASSEMBLY LAB
Experiment 7 / Interrupt + ADC + PWM integrated project
Final requirement: the potentiometer controls brightness and a button toggles the entire LED system
SYSTEM ARCHITECTURE
Potentiometer
PC0 / ADC0
ADC0
ADCH
OCR0A
PWM
LED
PD6 / OC0A
Button
PD2 / INT0
INT0 ISR
ON / OFF state
r20
HARDWARE MODIFICATION
1. Keep pot ends at +5 V and GND. Keep wiper at PC0 / ADC0.
2. Keep PWM LED at PD6 / OC0A.
3. Add push button: PD2 / INT0 → button → GND.
Experiment 7 / final integrated system
15

## Slide 16
EXPERIMENT 07 / AVR ASSEMBLY LAB
Experiment 7 / Integrated project code / setup + main
Part 1 of 2. The vector table, stack, PWM, ADC, button and main loop
EXPERIMENT 7 / COMPLETE CODE 1 OF 2
.include "m328pdef.inc"
; INTERRUPT VECTOR TABLE
.org 0x0000
rjmp RESET
.org INT0addr
rjmp INT0_ISR
.org 0x0034
RESET:
; Stack initialization
ldi r16, HIGH(RAMEND)
out SPH, r16
ldi r16, LOW(RAMEND)
out SPL, r16
; PWM setup on PD6 / OC0A
sbi DDRD, PD6
ldi r16, (1<<COM0A1) | (1<<WGM01) | (1<<WGM00)
out TCCR0A, r16
ldi r16, (1<<CS01) | (1<<CS00)
out TCCR0B, r16
; ADC setup: AVcc, left adjusted, ADC0
ldi r16, (1<<REFS0) | (1<<ADLAR)
sts ADMUX, r16
ldi r16, (1<<ADEN) | (1<<ADPS2) | (1<<ADPS1) | (1<<ADPS0)
sts ADCSRA, r16
; Button on PD2 / INT0
cbi DDRD, PD2
sbi PORTD, PD2
ldi r16, (1<<ISC01)
sts EICRA, r16
sbi EIMSK, INT0
; Initial state = ON
ldi r20, 1
sei
MAIN:
tst r20
breq SYSTEM_OFF
; Start ADC conversion
lds r16, ADCSRA
ori r16, (1<<ADSC)
sts ADCSRA, r16
WAIT_ADC:
lds r16, ADCSRA
sbrc r16, ADSC
rjmp WAIT_ADC
; ADC to PWM
lds r17, ADCH
out OCR0A, r17
rjmp MAIN
VERIFY BEFORE RUNNING
Vector table routes RESET and INT0
Stack is ready before PUSH and POP
PD6 carries hardware PWM
PD2 uses an internal pull-up
SEI enables global interrupts
The ISR code continues on the next slide.
Experiment 7 / vector table, setup and MAIN
16

## Slide 17
EXPERIMENT 07 / AVR ASSEMBLY LAB
Experiment 7 / Integrated project code / off state + ISR
Part 2 of 2. The system-off branch and a safe external-interrupt service routine
EXPERIMENT 7 / COMPLETE CODE 2 OF 2
SYSTEM_OFF:
clr r16
out OCR0A, r16
rjmp MAIN
INT0_ISR:
; Save R16
push r16
; Save status register
in r16, SREG
push r16
; Toggle system state
ldi r16, 1
eor r20, r16
; Restore SREG
pop r16
out SREG, r16
; Restore R16
pop r16
reti
ISR SEQUENCE
1
PUSH R16
protect working register
2
Save SREG
preserve flags
3
EOR R20, R16
toggle ON / OFF
4
Restore
reverse the save order
5
RETI
return to MAIN
Run and observe: press the button once, then move the potentiometer. The LED should switch off, then resume the mapped brightness after the next press.
Experiment 7 / PUSH, SREG, EOR, POP and RETI
17

## Slide 18
AVR ASSEMBLY LAB / SIMULIDE
Student challenge and submission
Modify the integrated project and demonstrate the result
YOUR TASK
Challenge brief
Modify the integrated system so that the button changes the behavior in a visible way. Examples: reverse the button polarity, cap the maximum brightness, or make the LED blink when the system is off.
Explain which register, bit, flag or branch you changed.
WHAT THE SEQUENCE BUILT
1
GPIO output
2
Loops and delay
3
GPIO input
4
Bit shift
5
Timer0 PWM
6
ADC to PWM
7
Interrupt plus ADC plus PWM
Your code grows from simple GPIO instructions to a system with PWM, ADC and interrupts.
Before you submit, name the signal path from potentiometer to LED and the path from button to ISR state.
Student challenge and submission
18

## Slide 19
AVR ASSEMBLY LAB / SIMULIDE
Student troubleshooting guide
Use this checklist before you change more code or ask for help
CHECK THESE FIRST
Confirm that AVRA built the current .asm file without errors
Load the matching .hex file into the ATmega328P in SimulIDE
Check the selected pin and the matching DDR, PORT or PIN register
Inspect one layer at a time: source, register, pin, component
Save a working copy before you start the next experiment
COMMON FAILURE POINTS
LED never lights
Check LED orientation, resistor path and DDR bit.
Button logic looks reversed
Pull-up means released is HIGH and pressed is LOW.
No PWM waveform
Check PD6, OC0A, COM0A1, WGM bits and timer clock.
ADC value stays fixed
Check the wiper on PC0, AVcc reference and ADSC wait.
Interrupt does not fire
Check PD2 pull-up, falling edge, EIMSK, SEI and RETI.
Debug in this order: source code, assembled hex, device selection, register state, pin state, component wiring.
Student reference / debug one observable layer at a time
19

## Slide 20
AVR ASSEMBLY LAB / SIMULIDE
Appendix: instruction and register progression
Keep this reference open while you write and debug your assembly programs
INSTRUCTION VOCABULARY
Start
LDI OUT IN SBI CBI RJMP
Control flow
DEC BRNE RCALL RET CPI
Peripheral access
LDS STS ORI SBIC SBRC
Interrupt safety
PUSH POP SEI EOR RETI
REGISTER CHEAT SHEET
DDRB / DDRD
pin direction
PORTB / PORTD
output and pull-up
PINB / PIND
read physical pins
TCCR0A / TCCR0B
Timer0 mode and clock
OCR0A
PWM duty value
ADMUX / ADCSRA
ADC reference, start and prescaler
ADCH
left-adjusted ADC high byte
EICRA / EIMSK
INT0 edge and enable
SREG
status flags saved in ISR
This lab ends with GPIO, loops, inputs, PWM, ADC and interrupts. Keep the circuit and code for later extensions.
Appendix / quick reference
20